Register Map for the OpenHT
Wojciech Kaczmarski, SP5WWP
M17 Project, April 2023
# Control registers
## Control register 1
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
0x0000	SSB	MOD			IO0_SRC			RESERVED			PD	DEMOD			BAND
0x0000	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW

Bits [1:0] – BAND – select operating band by using one of the DDR receivers
BAND	Value	Description
	0x0	sub-GHz (default)
	0x1	2.4 GHz
	0x2	invalid
	0x3	invalid

Bits [4:2] – DEMOD – select the demodulator
DEMOD	Value	Description
	0x0	FM (default)
	0x1	AM
	0x2	SSB
	0x3 to 0x7	reserved

Bit [5] – PD – Phase dithering for the FM transmitter submodule
PD	Value	Description
	0x0	phase dithering disabled (default)
	0x1	phase dithering enabled

Bits [8:6] – RESERVED
RESERVED	Value	Description
	0x0	-
	0x1 to 0x7	-

Bit [11:9] – IO0_SRC – IO0 signal source mux
IO0_SRC	Value	Description
	0x0	logic low (default)
	0x1	DRDY signal
	0x2 to 0x7	reserved

Bits [14:12] – MOD – select modulation
MOD	Value	Description
	0x0	FM (default)
	0x1	AM
	0x2	SSB
	0x3 to 0x7	invalid

Bit [15] – SSB
SSB	Value	Description
	0x0	USB (default)
	0x1	LSB

## Control register 2
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
0x0001	-	-	-	-	-	-	-	-	CTCSS_TX						STATE
0x0000	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW

Bits [1:0] – STATE – set the FPGA to one of the operating modes
STATE	Value	Description
	0x0	idle (default)
	0x1	TX
	0x2	RX
	0x3	reserved

Bits [7:2] – CTCSS_TX – set the transmitter’s CTCSS frequency (in hertz)
CTCSS_TX	Value	Description
	0x00	disabled (default)
	0x01	67.0
	0x02	69.3
	...	...
	0x3F	254.1

Bits [15:8] – reserved.

## I branch offset null
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
0x0002	MSB	16-bit signed integer														LSB
0x0000	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW

Signed 16-bit value to be added to the I branch after applying predistortion.
## Q branch offset null
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
0x0003	MSB	16-bit signed integer														LSB
0x0000	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW

Signed 16-bit value to be added to the Q branch after applying predistortion.
## I branch linear gain
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
0x0004	MSB	16-bit signed integer														LSB
0x4000	0	1	0	0	0	0	0	0	0	0	0	0	0	0	0	0
	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW

Signed, fixed-point, 16-bit gain value to be applied to the I branch. 0x4000 corresponds to +1.0 (default value).
## Q branch linear gain
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
0x0005	MSB	16-bit signed integer														LSB
0x4000	0	1	0	0	0	0	0	0	0	0	0	0	0	0	0	0
	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW

Signed, fixed-point, 16-bit gain value to be applied to the Q branch. 0x4000 corresponds to +1.0 (default value).

## Digital predistortion register 1
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
0x0006	MSB	16-bit signed integer														LSB
0x4000	0	1	0	0	0	0	0	0	0	0	0	0	0	0	0	0
	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW

Polynomial coefficient p_1 value of the formula below:
D(x) = p_1 x + p_2 sgn(x) x^2 + p_3 x^3
Signed, fixed-point value, where 0x4000 equals positive unity, “+1.0” (default value). This applies to all 3 registers holding the predistortion coefficients. To disable the predistortion, set p_1 to 0x4000 (+1.0) and both p_2 and p_3 to 0x0000 (0.0).
## Digital predistortion register 2
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
0x0007	MSB	16-bit signed integer														LSB
0x0000	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW

Polynomial coefficient p_2 value. See 1.5 for details. Default value is 0x0000 (zero).

## Digital predistortion register 3
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
0x0008	MSB	16-bit signed integer														LSB
0x0000	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW

Polynomial coefficient p_3 value. See 1.5 for details. Default value is 0x0000 (zero).

# Modulators
## Frequency modulator
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
0x0009	MSB	16-bit signed integer														LSB
0x0000	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW

Instantaneous frequency control word, signed.

## Amplitude modulator
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
0x000A	MSB	16-bit unsigned integer														LSB
0x0000	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW

Instantaneous amplitude control word, unsigned.

## SSB modulator
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
0x000B	MSB	16-bit signed integer														LSB
0x0000	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW

--

## Reserved 1
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
0x000C	RESERVED
0x0000	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW	RW

--

# Status registers
## Status register 1
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
0x000D	REV
0x4854	0	1	0	0	1	0	0	0	0	1	0	1	0	1	0	0
	R	R	R	R	R	R	R	R	R	R	R	R	R	R	R	R

Readback only register. This is mostly for fun or to check if the SPI comms are OK. Can be used to store revision number. The default REV value decodes to “HT”.

## Status register 2
	15		14		13		12		11		10		9		8		7		6		5	4	3	2	1	0
0x000E	-	-		-		-		-		-		-		-		-		-		-		-	-	-	PLL1	PLL0
0x0000	0		0		0		0		0		0		0		0		0		0		0	0	0	0	0	0
	R		R		R		R		R		R		R		R		R		R		R	R	R	R	R	R

Values in this register are reset to 0x0000 at start-up and get updated in realtime.

Bit [0] – PLL0 – Phase locked loop lock flag (38, 64, 152 MHz clocks)
PLL0	Value	Description
	0x0	PLL unlocked (default)
	0x1	PLL locked

Bit [1] – PLL1 – Phase locked loop lock flag (7.2 MHz sample rate generator master clock)
PLL1	Value	Description
	0x0	PLL unlocked (default)
	0x1	PLL locked

Bits [15:2] – reserved.

# Demodulators
## Frequency demodulator register
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
0x000F	MSB	16-bit signed integer														LSB
0x0000	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
	R	R	R	R	R	R	R	R	R	R	R	R	R	R	R	R

--

## Amplitude demodulator register
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
0x0010	MSB	16-bit unsigned integer														LSB
0x0000	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
	R	R	R	R	R	R	R	R	R	R	R	R	R	R	R	R

--
# Debug, raw readback
## I branch sample
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
0x0011	MSB	16-bit signed integer														LSB
0x0000	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
	R	R	R	R	R	R	R	R	R	R	R	R	R	R	R	R

Raw I branch sample, 16-bit, left justified, signed. Bits [2:0] are always zero.
## Q branch sample
	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
0x0012	MSB	16-bit signed integer														LSB
0x0000	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
	R	R	R	R	R	R	R	R	R	R	R	R	R	R	R	R

Raw Q branch sample, 16-bit, left justified, signed. Bits [2:0] are always zero.

# Registers summary
Read/write register
Read-only register
Address	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0	Page(s)
0x0000	SSB	MOD			IO0_SRC			RESERVED			PD	DEMOD			BAND		tbf
0x0001	-	-	-	-	-	-	-	-	CTCSS_TX						STATE		tbf
0x0002	MSB	16-bit signed integer														LSB	tbf
0x0003	MSB	16-bit signed integer														LSB	tbf
0x0004	MSB	16-bit signed integer														LSB	tbf
0x0005	MSB	16-bit signed integer														LSB	tbf
0x0006	MSB	16-bit signed integer														LSB	tbf
0x0007	MSB	16-bit signed integer														LSB	tbf
0x0008	MSB	16-bit signed integer														LSB	tbf
0x0009	MSB	16-bit signed integer														LSB	tbf
0x000A	MSB	16-bit unsigned integer														LSB	tbf
0x000B	MSB	16-bit signed integer														LSB	tbf
0x000C	RESERVED																tbf
0x000D	REV																tbf
0x000E	-	-	-	-	-	-	-	-	-	-	-	-	-	-	PLL1	PLL0	tbf
0x000F	MSB	16-bit signed integer														LSB	tbf
0x0010	MSB	16-bit unsigned integer														LSB	tbf
0x0011	MSB	16-bit signed integer														LSB	tbf
0x0012	MSB	16-bit signed integer														LSB	tbf